## Slide 1
INTRODUCTION TO PETROLEUM GEOLOGY
Application of Geoscience to the exploration and development of oil and natural gas
Oil and Gas = Naturally Occurring Hydrocarbon compounds derived from biogenic sediment
Hydrocarbon fossil fuels are associated with ancient sedimentary environments and sedimentary rocks

## Slide 5
Organic Sediment: Marine vs. Non-Marine
Bitumen – soluble organic matter
Kerogen – insoluble organic matter
Marine Organics: algal, soft parts, petroleum generation
Terrestrial Organics: woody plants, gas generation
Mixed Marine-Terrestrial: waxy oil-gas mix
Conditions for petroleum accumulation:
Organic source rock
Sediment burial and thermal maturation (heating over time)
Permeable and Porous reservoir rock to store fluids
Cap rock or impermeable seal to contain buoyant fluids
Favorable geometric arrangement between reservoir and seal

## Slide 6
Fossil Fuels:
-Preserved Organic Carbon
-Ancient Fossil Life
-Sedimentary Rock Record
Terrestrial Environments
Marine Environments

## Slide 7
Cable Tool Drilling
Early exploration method: drill the creeks and anticlines
Historical Perspectives
1859 “Drakes Well” Titusville, Pennsylvania
“Venango Sands Reservoir”
Greeks & Europeans through 17th century; petroleum collections at seeps and springs

## Slide 17
Depositional Environment
*Burial (1000’s of meters)
*Time (10^5-10^8 yrs)
*Heat (100 – 300 C)
*Pressure (MPa)

## Slide 18
Elemental composition of crude oil by weight%

## Slide 19
Hydrocarbon Compounds in Petroleum:
> 200 organic carbon-based compounds
Paraffins (CnH2n+2): trellis structure gaseous
Napthenes: simple ring structure, liquid
Aromatics: complex ring structure
Asphaltics: heavy oil and tar
Paraffins
Napthenes
Aromatics