## Slide 1: Athabasca Oil Sands
Ryan Johnson

## Slide 2: Where are the athabasca oil sands?
Northeast Alberta, Canada

## Slide 3: What’s So Significant?
1.8 trillion bbl of resources in northeast Alberta
  1 trillion bbl contained in Athabasca oil sands
Located at outcrop level or shallow depth
  Location known from direct observation prior to Geological Survey of Canada descriptions
    1875
  Tar pits

## Slide 4: What’s the problem?
Petroleum trap is elusive
Trap destroyed due to continued flexural loading
  Uplift and erosion
Confusion as to how petroleum was held in place over such a large area

## Slide 5: Approach
Use a paleohorizon to examine historical orientation of the layers during charge of oil
  Well data (70,000+ well picks)
Identify charge timing of regions of the Athabasca oil sands
Use bitumen-water contact to further confirm orientation of the region
Use kimberlite age dating to correlate with charge timing of oil sands
  Was used after study was finished, but good blind test

## Slide 6: History
Western Canada Sedimentary Basin (location of Athabasca oil sands) formation
  Precambrian rifting
  Paleozoic thermal subsidence along passive margin (western NA)
Megasequences
  Paleozoic carbonates, evaporates, and shales
    Exshaw Formation (source rock)
  Late Mississipian to Late Jurassic transitional meagsequence (subdued subsidence)
    Siliciclastic-dominated succession
    Gordondale (source rock)

## Slide 7: History – Megasequences cont.
Late Jurassic shift to flexural subsidence by Rocky Mountain fold and thrust belt
  Siliciclastic-dominated sequence
  Mannville Group (reservoir rock)
    McMurray Formation (fluvial-estuarine sands)
    Wabiskaw Member (marine sands)
    Capped by Clearwater Formation (shale)
      Marine transgression
Overlain by Colorado Group (marine sediments) at Athabasca oil sands
Continuation of flexural subsidence through early Eocene

## Slide 8: History

## Slide 9: Petroleum formation
Source maturity peak at Late Cretaceous
  Flexural loading led to maximum burial
Migration of oil hundreds of kilometers from west to east
Petroleum contained mostly in Mannville Group
Athabasca oil sands too shallow to pasteurize
  Never exceeded 45°C
  Biodegradation to bitumen
Coeval charge and biodegradation
  Formation of bitumen before tilting

## Slide 10: Reconstruction of trap
Colorado Formation used for reconstruction
  Formed around 84 Ma
Presence of a major four-way anticline in central Athabasca area
  285 km x 175 km
  60 m amplitude (240-300 m depth)
  Primary structural trap in Athabasca area
In addition to coeval charge and biodegradation, bitumen distribution controlled by structural and stratigraphic trap elements

## Slide 12: Trap domains
Athabasca area split into 6 distinct domains
  Central Athabasca (structural trap)
    44% of Athabasca oil sands by area
    300 m closure
  Northeastern Athabasca (onlap trap)
    Shallowest trap edge (200m or less)
    270 m lower limit
    Tarry bitumen outliers
      Leakage at pinch-out

## Slide 13: Trap Domains Cont.
Northern Athabasca (bitumen trap)
  Below 270 m
  Late charge of oil contained by bitumen already emplaced
Other bitumen traps
  Southern & Southwestern Athabasca, and Wabasca
    Below 300 m spillpoint
    Also represent late charge of oil

## Slide 14: Trap domains

## Slide 15: Bitumen-water contact
Defines contact line between bitumen and water separation due to density differences
Local variations in each trap domain
  Conforms with paleostructure reconstruction
Differences in elevation back interpretations of charge order
  Central filled first
  Northeastern onlap trap second
  Followed by deeper peripheral bitumen traps

## Slide 16: Restored Paleostructure

## Slide 17: Kimberlite
Numerous Late Cretaceous and Paleocene kimberlite pipes
Radiometric dating have been determined
  Spatial and temporal relationship to bitumen
3 drill holes with bitumen
  “Soaked” in bitumen
  Petroleum charge after intrusion of kimberlites
Age dated at 78-70 Ma
  2 at almost exactly 300 m closing contour
  1 at 334 m (northern trap domain)
Reinforces 84 Ma charge of anticline
Northern trap charged no earlier than 78 Ma

## Slide 18: Kimberlite Pipe

## Slide 19: Conclusion of events
1. Filling of the Central Athabasca four-way anticline (84 Ma)
  Coeval charge and biodegradation led to impermeable bitumen (no gas cap)
2. Filling of Northeastern Athabasca onlap trap
  Shallowest and first to fill after spillpoint of the anticline was breached
  Shallow depth also led to gas accumulation
3. Filling of peripheral bitumen traps (No earlier than 78 Ma in north)
  Updip bitumen seal
4. Erosion from Eocene to present
  Preservation of trap due to rapid rate of biodegradation to bitumen
  Tarry bitumen leaks onto surface where erosion has reached the reservoir and at onlap edge

## Slide 20: Conclusion of events