## Slide 1: Breaching of Condit Dam Wilcox et al.
Prepared by: Dylan Castle

## Slide 2: Overview of Condit Dam
White Salmon River, Washington
5.3 km upstream from Columbia River
Drains a 990 km2 area in Cascade Range
Reservoir trapped 1.6 million m3 of water and 1.8 million m3 of sediment
Sediment yield ~30 tonnes km-2 yr-1
Breached by explosives at bottom of dam

## Slide 4
- Largest intentional abrupt breaching of a dam, at time of removal
- Sediment made of 60% sand, 35% silt and clay, and 5% gravel

## Slide 5: Breaching
Most water flowed out within 90 minutes of breach, surface dropped 30 meters.
Initial drawdown exposed saturated, fine-grained sediment on 30-55 degree slopes.
Exposure triggered slope failures
Failures liquefied to form slurries

## Slide 6: High Intensity Flows
Typical base flow was ~20 m3 s-1
Flow reached peak discharge of 421 m3 s-1
Hour after peak discharge flow was down to 55 m3 s-1
After only two hours, 1260,000 m3 of sediment had evacuated from the reservoir, equaling about 10% or total volume
1.1 million m3 had flowed after 92 minutes

## Slide 7: Sediment Transport
Base transport between 5 and 15 mg/L
Concentrations increased to 3000 mg/L at peak discharge
53 minutes after breach concentrations increased to 850,000 mg/L (0.85 kg)
92 minutes after breach, 260,000 tonnes of suspended sediment had been transported

## Slide 9: Aggradation
Very little net aggradation from breach
Base aggradation was 1.5 m before breach
Maximum aggradation reached a stage height of 2.4 m
6 hours after breach, flow stage had dropped to 1.3 m, almost base levels.

## Slide 10: Conclusion
https://www.youtube.com/watch?v=4LxMHmw3Z-U