## Slide 1: Fluvial Hydrology, Fish Passage, and Sedimentation
Ryan Johnson
Earth and Physical Science Department
Western Oregon University
Monmouth, Oregon
Email: rjohnson11@wou.edu

## Slide 2
Outline
Introduction
River Hydrology
  Stream Flow
  Sediment Transportation
Salmonid in the Pacific Northwest
  Life-Cycle
Passage Blockage
Summary

## Slide 3: Salmonid Species and Rivers
Numerous species in Pacific Northwest
  Anadromous
  Freshwater
Complex relationships
  Habitat conditions
  Spawning sediment

## Slide 4
RIVER HYDROLOGY

## Slide 5: What does a river want to do?
Equilibrium
Energy In = Energy Out
Balance of deposition and erosion

## Slide 6: Controlling Factors
Climate & Geology
  Influence ecosystem components
Primary Factors
  Soil
  Vegetation
  Water

## Slide 7: Stream Morphology
Controlled by:
  Stream Energy
  Water Supply
  Sediment Transport
  Structural Elements

## Slide 8
Braided Stream vs.
Meandering Stream

## Slide 9: Sediment Transport
More Energy -> Larger Caliber Sediment
  Coarse gravel deposits
Less Energy -> Smaller Caliber Sediment
  Fine sand/silt deposits
Sediment Traps
  Creates complex energy environments

## Slide 10: Channel Bed Configuration
  Silt/Clay - Low Energy
  Sand - Low-Moderate Energy
  Gravel - High Energy

## Slide 11
SALMONID IN THE PACIFIC NORTHWEST

## Slide 12: Spawning Sediment
Salmonid preferences
  Mostly small gravel
  Some larger gravel
  Rounded

## Slide 13: Excessive Fine Sediment
Buries spawning gravel
Blocks pore spaces between gravel
  Lowers dissolved oxygen for eggs
  Displaces primary food source

## Slide 14: Fish Migration and Passage
Require unimpeded access
  Reproduction, feeding, and refuge
Passage timing, frequency, and duration
Migration and residence time

## Slide 15: Major Salmonid Migration in the Pacific Northwest

## Slide 16
MIGRATION BARRIERS

## Slide 17: Stream Crossings
Humans like to traverse streams
  Need to maintain river flow
Two primary solutions:
  Bridges
  Culverts
MIGRATION BARRIERS

## Slide 18: Bridges
Depends on design
Usually minimal impact
  Can trap large woody debris
Can be costly

## Slide 19: Culverts
Usually cheap and easy to install
Prone to becoming blocked
  Restoration is simple
Culvert configuration important

## Slide 20: Culvert Configuration is Important!

## Slide 21: Washington Blockages, 2004
2,256 road crossings of fish-bearing streams
  1,036 considered barriers
Estimated >33,000 salmonid blockages

## Slide 22: Dams
Used to control discharge within a stream
Very invasive to fish
  Blocks fish passage

## Slide 23: Solutions
Most effective is removal of dam
Fish ladders
  Gradual steps, traversed by jumping

## Slide 24: Salmon Cannon!

## Slide 25: Summary
Stream Hydrology: energy in = energy out
  Stream energy controls sedimentation
Salmonid require proper sediment for spawning
Salmonid need access to rivers and tributaries to complete life cycle
Human crossings can block fish passage if not maintained
  Restoration required
Youtube - Meet the Salmon Canon

## Slide 26
Five-Minute River Interlude
https://www.youtube.com/watch?v=8Jq1U8JyHW4
Youtube - Salmon Spawning