## Slide 1: Re-Meandering Of Lowland Streams: Will Disobeying the Laws of Geomorphology Have Ecological Consequences? Pedersen, Kristensen, Friberg, 2014, PlosOne, Volume 9, 1-10
Katie Halvorson

## Slide 2: Overview
Introduction to area
Methods and ideas on project
Results from project
Summary

## Slide 3: Where the study was done
Catchment areas of Jutland, Denmark

## Slide 4: Jutland areas based on last glaciation
Western: ice-free
Eastern: sub-glacial loamy moraine

## Slide 5: Key Ideas:
Determine how natural streams and rivers are structured
  Physical habitat
  Flow
  Sediment regime
  Improve ecological status of bodies of water in Europe

## Slide 6: The goal:
“All restoration measures were aimed at creating a more heterogeneous and natural stream reach.”

## Slide 7: Morphology of river depends on:
Catchment–scale controls
  Hydrology, geology
Differences in channel pattern at reach scale
  local slope, geology
Variations in structure and composition
  bank material, flow, and turbulent structure

## Slide 8: The study:
18 reaches selected
  6 natural meandering streams with little alterations
  6 channelized
  6 formally channelized
Field work done over 40days in April and May 2002

## Slide 9: Looked at:
Water chemistry
Physical habitats
Macroinvertebrates

## Slide 10: Results:
Composition of stream bed varied significantly among stream types.
  Cobble and pebble dominant in restored streams
  Sand in natural and channelized streams

## Slide 11: Results cont.
Natural streams width variation was significantly higher than in channelized streams.
Macroinvertebrate communities differed in species by stream type.

## Slide 12: Results cont.
Huge change in physical habitats of the restored streams (pebble and gravel) compared to natural and channelized streams (sand).
Stream bed slope differed between the three
  High slopes = restored
  Lowest = channelized

## Slide 13: In summary:
Natural functioning of the geomorphological process is affected by both channelization and restoration and that restoration DOES NOT re-establish the natural functioning at a 3+ year time-scale.