## Slide 1: Oregon Case Studies
Ryan Johnson

## Slide 2: Studies
The response of impounded sediment to a culvert replacement project on Sutter Creek, a tributary of Honey Grove Creek, in the Alsea River Basin of the Central Oregon Coast Range
East Fork Williams Creek sediment analysis/East Fork private road inventory and sediment analysis, 2003, C. Rodgers, Williams Creek Watershed Council

## Slide 3: Sutter Creek
Located in Alsea River Basin
Tributary of Honey Grove Creek
Small floodplain upstream of road on both sides
Fluvial or lacustrine? Combination?

## Slide 5: Study
Effect of culvert at Honey Grove Road crossing on sedimentation of Sutter Creek
Impounding of water upstream of crossing
Incising channel upstream of crossing

## Slide 6: History
Long history of logging
  Douglas Fir
  Active since WWII
Basin has been clear-cut since 1950
Significant soil erosion
Culvert present since at least 1940’s
  Replaced multiple times

## Slide 8: Methods
Characterization of floodplain and channel bed sediments
  Transects established across impounded sediment surface
  Clam gun used at several points across transect
Channel topography survey
Discharge measured
  Stage & flow velocity
Measurement of sediment transport
  Bedload & suspended load

## Slide 10: Data Analysis
2D Analysis of stream cross-section
  Significant drop in bed elevation during high flows
3D Analysis of sediment volumes eroded
  ArcGIS
Calculation of discharge rating curve
Calculation of median grain size for floodplain and channel bed samples

## Slide 11: Results
Still many unknown relationships between events
  Logging vs. installation of road
  Depth of valley floor prior to disturbances
Mobilization of fines during storm event
  Collection upstream of road
  Cohesion and compaction
Impounded sediment deposited into standing water
Intent to continue actively studying area

## Slide 12: East Fork Williams Creek
Siskiyou Mountains of southwestern Oregon
Mostly forestry land use within the watershed
Watershed contains 67 potential sensitive species

## Slide 14: Purpose
Address observations of high sediment loads in East Fork Williams Creek
Study conditions of private roads an their impact on sediment delivery to local streams in East Fork branch
Determine non-point sediment sources

## Slide 15: Problem
Recognized as source for high sediment loads
  During heavy rain events
DEQ listing as “streams exceeding water quality standards”
Channelization and instream wood removal
  No floodplain relief
  Excessive discharge during high flows
  Can remove acres of land within hours

## Slide 16: Erosion/Sedimentation Sources
Private roads
Culvert diversions along roads
Ditches along roadbeds
Over-steepened road cuts
Runoff from grazing lands
Degraded farm roads
Excessive livestock riparian zone
Reduced riparian vegetation
Intrusive igneous rock (fine sediment)

## Slide 17: Upper East Fork Road erosion

## Slide 18: Fine sediment runoff during rainstorm

## Slide 19: Methods
Data collection of conditions of private roads
Ditch and culvert conditions
Turbidity levels during high water at 12 locations
Bedload samples in several tributaries
Cross-sections at select locations
Wolman pebble counts
Observation of erosion sites and unstable stream banks
Combined with geologic mapping
  Identify rock types contributing greatly to sedimentation

## Slide 20: Solutions
Road improvement or decommission
  Most effective option
Revegetation
Reduction of grazing in riparian zones
Erosion control structures
Restoration of stream bank habitat

## Slide 21: Road repair in progress

## Slide 22: Conclusion
Sutter Creek
  Impounded sediment upstream of road crossing culvert
  Downcutting of channel upstream of culvert
  Further study underway
East Fork Williams Creek
  Excessive sediment transport
  Main cause unmaintained private roads
  Repair of roads, and maintenance of ditches and culverts show positive results
  Further road work intended