## Slide 1
Local & Downstream Impacts of Contemporary Forest Harvesting Practices on Watershed Hydrology
Nicolas Zègre
Forestry & Natural Resources
West Virginia University
Notes: Thanks for coming everyone, nice to see another solid turn out. I think it’s the controversial issues that really brings people out, and I think we’ve got the granddaddy of em all. So we’re going to talk about ___.
This is sort of rough go through of my proposal presentation. I’ve added some base information for a broader audience so hopefully what is presented will register with most everybody. That said, if you have questions related to something that didn’t make sense, I would encourage you to ask during the presentation rather than waiting till the end so everybody tracking along. Mindful of time, but I’d rather keep people engaged throughout.

## Slide 2
  Arne Skaugset |Amy Simmons |Hazel Owens
        Oregon State University
Co-authors, Collaborators, & Acknowledgements
  Roseburg Forest Products
  Dan Newton |Dick Beeby
  Nicholas Som|Lisa Ganio
  USFW & Oregon State University
Notes: This is just sort of a quickie outline highlighting the major components of the presentation.
I’ll present some basic info about the hydrologic cycle, specifically focusing on catchment hydrology.
Then I’ll introduce MTM into the equation and some of its impacts on hydrology.
Then I’ll talk about IH and how we can apply it to this question
Then we’ll get into the specifics of this study, what we’re trying to achieve and how we’ll do that.

## Slide 3
FOREST HARVESTING & HYDROLOGY
First catchment study – Wagon Wheel Gap, CO Bates [1921]
J. Rothacher - 1957
Ice & Stednick [2004]
Classic Western Studies –
  Oregon – Alsea |HJ Andrews |Coyote Creek
  California – Caspar Creek
OSU archives
Ice & Stednick [2004]
USFS – 1976
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 4
HINKLE CREEK PAIRED WATERSHED
Fill knowledge gaps of current forest harvesting practices
HINKLE CREEK
  Western foothills Oregon Cascades
  Owned and managed by Roseburg Forest Products
  60-yr harvest regenerated
  Parent geology is basalt and rhyolite flows
  Deep, well drained silty clay loams, clay loams, gravelly clay loams, and gravelly loams
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 5
HINKLE CREEK PAIRED WATERSHED
Study design – paired/nested
  Basin-scale
    North Fork Hinkle (reference)
    South Fork Hinkle (treatment)
  Headwater-scale
    2 reference
    4 treatment
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 6
HINKLE CREEK PAIRED WATERSHED
Study design
  Paired, nested watershed study
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 7
HINKLE CREEK PAIRED WATERSHED
Study design
  Paired, nested watershed study
  Evaluate for local & downstream changes
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 8
HINKLE CREEK PAIRED WATERSHED
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 9
HINKLE CREEK PAIRED WATERSHED
Study design – ~19 km2 |1,9oo ha 3rd order watershed
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 10
HINKLE CREEK PAIRED WATERSHED
Study design – HYDROMETRIC INSTRUMENTATION
  Basin-scale
    Measured by the USGS – 30 min
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 11
HINKLE CREEK PAIRED WATERSHED
Study design – HYDROMETRIC INSTRUMENTATION
  Headwater-scale
    modified Parshall flumes & pressure transducers (10 min)
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 12
Study design – HYDROLOGIC METRICS
HINKLE CREEK PAIRED WATERSHED
    Max. instantaneous peakflow
    Storm quick flow
    Mean monthly streamflow
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 13
Study design – HARVESTING TREATMENTS
    Pre-study harvest entry 2001 (11%)
HINKLE CREEK PAIRED WATERSHED
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 14
HINKLE CREEK PAIRED WATERSHED
Study design – HARVESTING TREATMENTS
  1st harvest entry 8/2005 – 4/2006
    Adjacent to non-fish bearing streams (type N)
    5 clearcut units (1.52 km2|380 acres)
    12.2 mmbf |3,281 loads of logs
65%
31%
13%
38%
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 15
Study design – HARVESTING TREATMENTS
HINKLE CREEK PAIRED WATERSHED
  2nd harvest entry 8/2008 – 3/2009
    Adjacent to small and medium (type F)
    4 clearcut units (1.31 km2|324 acres)
    7.6 mmbf |2,059 loads of logs
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 16
HINKLE CREEK PAIRED WATERSHED
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 17
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 18
HINKLE CREEK PAIRED WATERSHED
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 19
HINKLE CREEK PAIRED WATERSHED
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 20
LOCAL
PEAK FLOW
HARVESTING EFFECTS
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 21
LOCAL
QUICK FLOW
HARVESTING EFFECTS
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 22
LOCAL
MONTHLY
STREAM FLOW
HARVESTING EFFECTS
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 23
DOWNSTREAM
PEAK FLOW
QUICK FLOW
MONTHLY
STREAMFLOW
HARVESTING EFFECTS
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 24
HARVESTING EFFECTS
SEASONAL CHANGES
PEAK FLOW
**
*
**
*
* sig. 1 ref catchment
** sig. both ref catchments
- not sig α=0.05
-
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 25
HARVESTING EFFECTS
SEASONAL CHANGES
QUICK FLOW
* sig. 1 ref catchment
** sig. both ref catchments
- not sig α=0.05
*
**
*
**
*
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 26
SEASONAL CHANGES
MONTHLY STREAMFLOW
HARVESTING EFFECTS
* sig. 1 ref catchment
** sig. both ref catchments
- not sig α=0.05
**
**
*
**
*
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 27
  Significant increases in monthly streamflow, peak flow and quick flow at local scale
SUMMARY OF HYDROLOGY STUDY
  Significant increases in monthly streamflow and significant decrease in quick flow at downstream scale
  Seasonal changes:
    Greatest QF increases during summer / fall;
    Greatest Q increases during spring / summer
  Impact of harvesting on peak flows limited to storms < 2-yrs return
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 28
  Change detection at different time-scales (e.g. seasonal) & storm definition
CONTINUING & FUTURE WORK
  Quantify hydrologic recovery
  Models to generate hypotheses of process change
  Understand decreases in quickflow at downstream scale
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 30
STREAMFLOW
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 31
PEAK FLOW
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.

## Slide 32
QUICK FLOW
Notes: So another key component to quantifying hydrologic response residence time within a watershed.
So we’ll go to our animation again to demonstrate that each droplet of water will take a unique path to the outlet (if it isn’t evapotranspired), and from the distribution of all the transit times of these flow paths we can figure mean residence time within a waterhsed.
And these are important considerations for both water quality as contact time is a critical factor in biogeochemical reactions and water quantity in that mean residence time will describe how quick or flashy our storm response is.