## Slide 1: Local and Downstream Impacts of Contemporary Forest Practices on Sediment Yield
A Skaugset, N Zegre, A Simmons,
& H Owens

## Slide 2
Cast of Characters
Amy Simmons
Alex Irving
Nic Zegre
Dennis Feney
Tim Royer
Emily Sinkhorn
Matt Meadows
Chris Surfleet

## Slide 7: Sediment Yield Calculations
Discharge is very important to the calculation of sediment yield.
Sediment yield is highly skewed to the few days with the greatest discharge.
Sediment yield will be highly correlated to discharge.
Increases in water yield should correlate with increases in sediment yield.

## Slide 8: Regional Sediment Yield Values
Watershed Study | Year of data collection | Sediment Yield (kg/ha/yr)
HJ Andrews – WS2 | 57-76 | 18.4
Coyote Creek – WS4 | 66-79 | 76.5
Alsea – Flynn Creek | 59-73 | 162
Caspar Creek - NFC | 63-76 | 295
NFH | WY05 | 117
NFH | WY07 | 554
NFH | WY10 | 65
NFH | WY11 | 259
NFH - Ave | 05-11 | 249

## Slide 15: Watershed Study Sediment Yield Results
Watershed Study | Increase in Sediment Yield (kg/ha/yr) | Increase (%)
HJ Andrews – WS1 | 86 | 420
HJ Andrews – WS3 | 802 | 3,900
Alsea – Needle Branch | 251 | 325
Alsea – Deer Creek | 183 | 123
Caspar Creek - SF | 1,475 (1st yr increase) | 335
Caspar Creek - SF | 2,510 (6 yr increase) | 212
Caspar Creek - NF | 188 | 89

## Slide 17: Sediment Yield Results
Sediment yield results from contemporary forest practices are not consistent with the findings in the seminal literature.
Historically, sediment yield has doubled or tripled or greater vs contemporary increases in the 20 to 40% range.
Why is that?

## Slide 18: Buffer strips

## Slide 19: Clearcut size limits and adjacency constraints

## Slide 20
Skyline Logging Systems

## Slide 21
Site Preparation

## Slide 22
Location, construction, maintenance, and, especially connectivity, of roads.

## Slide 23: Transfer Processes in Steep Forested Catchments
Debris Avalanche
Litterfall
Root Throw
Slump or earthflow
Solution transport
Soil creep
Surface movement
Hillslope Process
Stream Channel Process
Dissolved load
Suspended load
Bed load
Debris torrent
Modified from Swanson et al., 1982

## Slide 24: What I Think I Think
Sediment yield result do not appear to be consistent with the findings in the seminal literature.
The results appear to be more muted, with increases in the 20% to 40% range.
These results are in agreement with and correlate with the increases in water yield.
A testable hypothesis is that the increase is due to increased stream power due to increased water yield.
An alternative hypothesis is that the increase is due to an increased erosion rate of the watershed due to logging.

## Slide 25
Douglas County
Thank You!